## Slide 1
Why Complex Numbers in AC?
CORE-001 | Visual summary
Audience: 1st-2nd year undergrads
Focus: physical meaning + applications
Outcome: phasor intuition
CORE-001 | English | Slide 1/20

## Slide 2
Learning Goals
Explain why AC needs complex numbers
Visualize phasors as rotating vectors
Convert time-domain to phasor
Interpret magnitude and phase
CORE-001 | English | Slide 2/20

## Slide 3
The Core Problem
Trigonometry (time-domain)
Long steps
Error-prone
Hard for many phases
Phasor (complex domain)
Compact math
Simple addition
Scales to big systems
CORE-001 | English | Slide 3/20

## Slide 4
Hook Visual: Split Screen
Left: long sinus equations
Right: short phasor sum
Same result, less work
CORE-001 | English | Slide 4/20

## Slide 5
Key Idea: Rotating Vector
Sine wave
Rotating vector
Projection
Sine wave = projection of a rotating vector
Phase = angle
Magnitude = length
CORE-001 | English | Slide 5/20

## Slide 6
Two Vectors at Once
V1 = 100, phase 0 deg
V2 = 80, phase 45 deg
Projections create two waves
CORE-001 | English | Slide 6/20

## Slide 7
Vector Addition
Tip-to-tail gives resultant
Result projection = summed wave
Much easier than sin(A)+sin(B)
CORE-001 | English | Slide 7/20

## Slide 8
Polar to Rectangular
Z = R cos(theta) + j R sin(theta)
Real axis = horizontal
Imag axis = vertical
CORE-001 | English | Slide 8/20

## Slide 9
Complex Plane
Real axis: resistive
Imag axis: reactive
j = 90 deg rotation
CORE-001 | English | Slide 9/20

## Slide 10
Euler for Phasor
Z = R * e^(j theta)
Compact form for magnitude and phase
CORE-001 | English | Slide 10/20

## Slide 11
Resistor Impedance
Z_R = R
No phase shift
CORE-001 | English | Slide 11/20

## Slide 12
Inductor Impedance
Z_L = j * omega * L
Voltage leads current by 90 deg
CORE-001 | English | Slide 12/20

## Slide 13
Capacitor Impedance
Z_C = -j / (omega * C)
Current leads voltage by 90 deg
CORE-001 | English | Slide 13/20

## Slide 14
Series RLC
Z = R + j(omega L - 1/(omega C))
Real part = R
Imag part = X
CORE-001 | English | Slide 14/20

## Slide 15
Magnitude and Phase
|Z| = sqrt(R^2 + X^2)
phase = arctan(X/R)
Meaning: size and timing
CORE-001 | English | Slide 15/20

## Slide 16
Quick Example
R=10, L=50 mH, C=100 uF, f=50 Hz
Z = 10 - j16.12 ohm
I = 11.6 A with phase +58.1 deg
CORE-001 | English | Slide 16/20

## Slide 17
Power Factor
Cos(phase) controls efficiency
Inductive: PF lagging
Capacitive: PF leading
CORE-001 | English | Slide 17/20

## Slide 18
Industry Applications
Load flow: complex bus voltages
Protection relay: R-X plane zones
Power quality: harmonic analysis
CORE-001 | English | Slide 18/20

## Slide 19
Simulation and Exploration
Change f and C to see phase shifts
Resonance when X_L = X_C
Phasor diagram as main tool
CORE-001 | English | Slide 19/20

## Slide 20
Wrap Up
Complex numbers = magnitude + phase
j = 90 deg rotation
Phasors simplify AC analysis
CORE-001 | English | Slide 20/20